## Slide 1: Get Better Fast: Mixture Analysis
Reverse Searching and NNLS

## Slide 2: Main Process Steps: Overview
1. Baseline Correction
2. Smoothing
3. Normalize spectrum with its max intensity
4. Peak detection with CWT
5. Query matches database majors peak  calculate match quality
6. Use NNLS on spectra with a certain MQ or better to estimate ratios
7. Standardize spectra

## Slide 3: Baseline Correction

## Slide 4: Baseline Correction II
In the past, common methods have been simple/modified polynomial fitting, penalized least squares (PLS) or weighted LS, wavelet using morphological erosion, derivatives, and robust local regression
PLS: Iteration weights are based on the sum squares errors (SSE) between the original signal and the last fitted baseline
New method of airPLS used to reduce Raman peak influence gradually

## Slide 5: Old Method Drawbacks
Simple polynomial fit: Not very effective, accuracy highly dependent on skill of user
Modified polynomial fit: Poor performance in low signal-to-noise and signal-to-background ratio environments
Penalized least squares: Peak detection reliant and can produce negative amplitudes for complex signals

## Slide 6: Old Method Drawbacks II
Wavelet: Baseline must be well-separated in the transformed signal domain (good in theory, worse in practice)
Derivatives: Change original peak shapes
Robust local regression: Baseline must be smooth and not too varying, also needs user input for bandwidth and tuning parameters
baselineWavelet package: poor sparse matrix and linear algebra supporting libraries in R limits signal size to 5k variables

## Slide 7: airPLS
Adaptive iteratively reweighted PLS is a procedure that gradually arrives at a baseline over several adjustments
Speedy, accurate, and flexible
Weight vector w:
Initialize w=1, each iterative w afterwards should be defined by:

## Slide 8: airPLS II
Continue reweighting w to fit z and performing more iterations until either the selected number of iterations has been performed, or stopping criterion has been reached:
Algorithm has a linear runtime due to using sparse matrix linear algebra techniques, ensuring good performance for large number of variables

## Slide 9: Smoothing
Fidelity: How close data sets are to each other. In this case, how similar is a fitted data set to the original? Measured by the SSE between them:
Roughness: How much does a data set change from point to point? Measured by sum of the squared differences:

## Slide 10: Smoothing II
Use a Whittaker smoother similar to the one outlined by “A Perfect Smoother” (Eilers 2003) based on penalized least squares
I is the identity matrix, D is the matrix of differentials, lambda is the smoothing parameter, x is the original spectrum vector, and z is the smoothed
User can adjust lambda, larger values give smoother fit, and smaller values give greater fidelity. Pick the one that minimizes cross validation error.

## Slide 11: Smoothing III
Cross-validation: Make partitions of sample observations from training data (validation sets). Fit a model to the training data and see how it does against each validation set
K-fold CV: Split observations into K partitions, train on K-1 partitions, test error predicted on excluded k-th partition
Leave One Out CV (LOOCV): (K=n) Partition a data set of n points into two disjoint sets so that a set of n-1 points estimates a singleton point. Iterate so each point in the n set is in the singleton exactly once.

## Slide 12: Normalization
Point-wise division of spectrum by its maximum y value (relative intensity)
The spectrum will then have y values between 0 and 1
Statistical method used to eliminate certain influences between different data sets

## Slide 13: Peak Detection
The next step in the process is to locate all the peaks on the query spectrum
Use Continuous Wavelet Transform (CWT) algorithm to detect peaks automatically
Resultant matrix C contains the wavelet coefficients, with s(t) as original signal with “a” scale and “b” shift

## Slide 14: Peak Detection II
The Ricker Wavelet is often chosen to be the mother wavelet for Raman spectra